# MVA – Object Recognition and Artificial Vision

# Assignment 3

# Eigenfaces for recognition

Jean-Baptiste Fiot
Nov 2008

# Algorithm outline
## Subtraction of the mean picture.
-
I_mean = 1 over {N_mean} {sum from{I in Training Set} I}
=
## Extraction of the principal components.
Notations:
- Training pictures: I_1, ..., I_M (M=280 here).
- Each picture I_i (N*N=32*32 here) is represented by a vector %PHI_i with N² elements.
- A = [%PHI_1 ... %PHI_M] (N² * M matrix)

Using the princomp.m function, we extract the principal components of the training pictures, namely N² vectors with N² elements each. The principal components are the eigenvectors of AAT.
Here are some of them:

To have a representation with a lower dimension, we keep only K (normalized) eigenvectors left lbrace u_1,...,u_K right rbrace , corresponding to the K largest eigenvalues.

We want to project the training pictures on vect(u_1,...,u_K) :
%PHI_i = sum from{1} to{K} %alpha_{i,j} u_j ~ forall i in left ldbracket 1,M right rdbracket
We get the coefficients with:
 %alpha_{i,j} = left langle %PHI_i mline u_j right rangle = %PHI_i^T u_j ~ forall (i,j) in left ldbracket 1,M right rdbracket times left ldbracket 1,K right rdbracket

## Recognition of an unknown face.
- We subtract the mean image of the training set:
  I_{unknown, centered} = I_unknown - I_mean
- We project the corresponding %GAMMA vector on vect(u_1,...,u_K) :
  %beta_j = left langle %GAMMA mline u_j right rangle = %GAMMA^T u_j ~ forall j in left ldbracket 1,K right rdbracket dlrarrow %GAMMA = sum from{1} to{K} %beta_j u_j
- We find the image whose low-dimension representation has the minimum Euclidian distance with the unknown picture's low-dimension representation:
  I_i recognized face dlrarrow d(%beta,u_i) = min lbrace d(%beta,u_i), i in ldbracket 1,M rdbracket rbrace
  I implemented EuclDistClassifier.m for this part.

# Interest of this method
A direct way to solve this problem would be to find the image which has the maximum NCC with the unknown picture.

Despite its relative loss of precision, the interest of the low-dimensional projection method relies on its computing efficiency. I implemented NNclassifier.m to compare both methods' performances.

With computations for all K in left ldbracket 1,50 right rdbracket , the “direct” method takes 380 seconds, and the low-dimensional projection method takes only 6 seconds. This means a 63 folds decrease.

# Results for K=100
For each group of 4 lines, we have:
- original test images
- low-dim test images
- low-dim nearest neighbors
- original nearest neighbor

The green faces are the correct recognitions, the red the incorrect ones.

# Classification rate
For a given K, the classification is given by:

R_classification = {Card [I in Test Set, Estimated Label(I) = Test Label(I) ]} over {N_test}

Here is classification rate's evolution depending on the dimension K:
(K could go up to N² (=1024 here), but the classification rate is not displayed for values higher than 300.)

Conclusion:
For low K, the performance is extremely bad, but rises very quickly, and tends to stagnate just below 90%.